## Slide 1: Quantifying North American methane emissions using satellite observations of methane columns Daniel J. Jacob
with
Alex Turner, Bram Maasakkers, Melissa Sulprizio, Kevin Wecht (Harvard)
Anthony Bloom, Kevin Bowman (JPL)
Tom Wirth, Melissa Weitz, Leif Hockstad, Bill Irving (EPA)
Robert Parker, Hartmut Boesch (U. Leicester)

## Slide 2: Importance of methane for climate policy
Present-day emission-based forcing of methane is 0.95 W m-2 (IPCC AR5), compared to 1.8 W m-2 for CO2
Climate impact of methane is comparable to CO2 over 20-year horizon
Methane controls provide a lever for mitigating near-term climate change
Controlling methane has additional benefit for air quality
Problem: large diversity
of poorly constrained sources
Livestock
110
Landfills
60
Gas
70
Coal
50
Rice
40
Other
30
Wetlands
160
Fires
20
Global sources,
EDGAR4.2+LPJ
(Tg a-1)

## Slide 3
High-resolution satellite-based inverse analysis system
to quantify methane emissions in North America
GEOS-Chem CTM and adjoint
1/2ox2/3o over N. America
nested in 4ox5o global
Satellite data
Bayesian
inversion
Optimized emissions at up to 50 km resolution
Validation
Verification
Suborbital data
Aircraft campaigns
Surface networks
Bottom-up (prior)
EDGAR v4.2 + LPJ
EPA
New wetlands
CMS publications so far:
Wecht et al. [JGR 2014]: inversion of SCIAMACHY data for 2004
Wecht et al. [ACP 2014]; inversion of CalNex data + OSSEs for TROPOMI, Geo
SCIAMACHY
2002-2005
TROPOMI
2016-
GOSAT
2007-
Geostationary
OSSE

## Slide 4: Indirect validation of GOSAT with suborbital data using GEOS-Chem prior as intercomparison platform
No GEOS-Chem background bias
vs. global suborbital data
Correction of GOSAT high-latitude bias
GOSAT
GEOS-Chem
minus
GOSAT
GEOS-Chem
minus
corrected
GOSAT
Turner et al. [in prep]
mean single-retrieval
GOSAT precision 13 ppb
R2 = 0.94
slope = 0.97
R2 = 0.62
slope = 0.98
R2 = 0.81
Slope = 0.92

## Slide 5: Balancing aggregation and smoothing inversion errors in selection of emission state vector dimension
Native-resolution 1/2ox2/3o
emission state vector x (n = 7096)
Aggregation matrix 
x =x
Reduced-resolution
state vector x (here n = 8)
Posterior error covariance matrix:
Aggregation Smoothing Observation
Choose n = 369 for negligible aggregation error; allows analytical inversion with full error characterization
10 100 1,000 10,000
Number of state vector elements
Mean error s.d., ppb
Posterior error
depends on choice
of state vector
dimension
observation
aggregation
smoothing
total
Turner and Jacob, in prep.

## Slide 6: Using radial basis functions (RBFs) with Gaussian mixing model as state vector
State vector of 367 Gaussian 14-D pdfs optimally selected from similarity criteria in native-resolution state vector
Each 1/2ox2/3o grid square is unique linear combination of these pdfs
This enables native resolution (~50x50 km2) for major sources and much coarser resolution where not needed
Dominant RBFs for emissions
In a Los Angeles 1/2ox2/3o gridsquare
Turner and Jacob, in prep.

## Slide 7: Global inversion of GOSAT data feeds boundary conditions for North American inversion
GOSAT observations, 2009-2011
Adjoint-based inversion
at 4ox5o resolution
Dynamic
boundary
conditions
Analytical inversion
with 369 Gaussians
Turner et al., in prep.
correction factors to EDGAR v4.2 + LPJ prior

## Slide 8: Posterior distribution of North American emissions
Averaging kernel matrix indicates 39 degrees of freedom for signal (DOFS)
Turner et al., in prep.

## Slide 9: Evaluation of posterior emissions with independent data sets In contiguous US (CONUS)
GEOS-Chem simulation
with posterior vs. prior emissions
Comparison of California results
to previous inversions of CalNex data
(Los Angeles)
Turner et al., in prep.

## Slide 10: Methane emissions in CONUS: comparison to previous studies, attribution to source types
Anthropogenic emissions are 50% higher than EPA national inventory
Attribution of underestimate to oil/gas or livestock is sensitive to assumptions on prior errors
Improve source attribution in the future by
  Better observing system (more GOSAT years, TROPOMI, SEAC3RS,…)
  Better bottom-up inventory (gridded EPA inventory, wetlands)
Ranges from
prior error
assumptions
Turner et al., in prep.

## Slide 11: Construction of a 0.1ox0.1o monthly gridded version of the EPA national bottom-up inventory
Use monthly state/county/GGRP/algorithm info from EPA, further distribute with data from other sources (USDA, EIA, DrillingInfo,…)
Done as collaboration between Harvard and EPA Climate Change Division
Provide improved prior for inversions and feedback to guide improvement in bottom-up inventory
EPA livestock
enteric emissions.
2012
Livestock (enteric)
EPA, 2012
Maasakkers et al., in progress
Livestock (enteric)
EDGAR, 2010
Livestock (enteric)
EPA-EDGAR

## Slide 12: Construction of a 0.1ox0.1o monthly gridded version of the EPA national bottom-up inventory
Livestock (manure)
EPA, 2012
Livestock (manure)
EDGAR, 2010
Livestock (manure)
EPA-EDGAR
Maasakkers et al., in progress
Use monthly state/county/GGRP/algorithm info from EPA, further distribute with data from other sources (USDA, EIA, DrillingInfo,…)
Done as collaboration between Harvard and EPA Climate Change Division
Provide improved prior for inversions and feedback to guide improvement in bottom-up inventory

## Slide 13: Construction of a 0.1ox0.1o monthly gridded version of the EPA national bottom-up inventory
Rice: EPA EDGAR Difference
Use monthly state/county/GGRP/algorithm info from EPA, further distribute with data from other sources (USDA, EIA, DrillingInfo,…)
Done as collaboration between Harvard and EPA Climate Change Division
Provide improved prior for inversions and feedback to guide improvement in bottom-up inventory
Maasakkers et al., in progress

## Slide 14: Construction of a global and N American wetland and rice bottom-up emissions inventory
Wetland Extent
MEaSUREs and GIEMS multi-satellite datasets
wetlands.jpl.nasa.gov, Shroeder et al., 2014, Prigent et al., 2007
Terrestrial biosphere models
MsTMIP model ensemble
Huntzinger et al., 2013
Wetland & Rice CH4 emissions model
Bottom up CMS wetland and rice CH4 emission inventory: global monthly 1x1 degree CH4 emission climatology.
Bloom et al., in progress